## Slide 1
ESP32
ESP32 GPS Weather Station
Automatic Approximate Location Detection · Real-Time Weather · OpenWeatherMap API
By: Techbots Acadmy | Platform: Arduino IDE | Board: ESP32 Dev Module

## Slide 2
Project Overview
What It Does
🌤
Connects to WiFi
Detects location via IP
Fetches weather data
Prints to Serial Monitor
Components Used
🔌
ESP32 Dev Module
WiFi
HTTPClient library
ArduinoJson library
APIs Used
🌐
OpenWeatherMap API

## Slide 3
System Architecture – Flow
ESP32 Powers On
setup() begins
▶
Connect to WiFi
SSID + Password
▶
Get IP Location
ip-api.com → lat, lon, city
▶
Get Weather
OpenWeatherMap API
▶
Print Results
Serial Monitor output
getLocation()
Uses free ip-api.com — no API key needed.
Returns: city, region, country, lat, lon.
getWeather()
Calls OpenWeatherMap with lat+lon.
Returns: place name, temperature (°C), weather.

## Slide 4
Step-by-Step: Initial Setup
01
Libraries
Include WiFi.h, HTTPClient.h, ArduinoJson.h in your sketch.
02
Credentials
Set ssid and password to your WiFi network name and key.
03
API Key
Paste your OpenWeatherMap API key into the apiKey string variable.
04
Serial Begin
Call Serial.begin(115200) in setup() to enable serial output.
05
WiFi Connect
Use WiFi.begin(ssid, password) and poll until WL_CONNECTED.
06
Call Functions
Call getLocation(), delay(2000), then getWeather() once in setup().

## Slide 5
Step-by-Step: getLocation() Function
// getLocation()
HTTPClient http;
String url = "http://ip-api.com/json/";
http.begin(url);
int code = http.GET();
String payload = http.getString();
DynamicJsonDocument doc(2048);
deserializeJson(doc, payload);
latitude = doc["lat"];
longitude = doc["lon"];
String city = doc["city"];
1
Create HTTP client
HTTPClient http; initialises the client object.
2
Set URL
ip-api.com/json/ is a free geo-IP API — no key needed.
3
Make GET request
http.GET() sends the request; returns HTTP status code.
4
Parse JSON
ArduinoJson reads the response and extracts fields.
5
Store lat/lon
Save latitude & longitude as global floats for getWeather().
6
Print details
City, Region, Country, Lat, Lon printed to Serial Monitor.

## Slide 6
Step-by-Step: getWeather() Function
// getWeather()
String url =
"https://api.openweathermap.org/"
"data/2.5/weather?lat=" +
String(latitude) +
"&lon=" + String(longitude) +
"&units=metric&appid=" + apiKey;
http.begin(url);
http.GET();
String payload = http.getString();
DynamicJsonDocument doc(4096);
deserializeJson(doc, payload);
String weather = doc["weather"][0]["main"];
float temp = doc["main"]["temp"];
String place = doc["name"];
1
Build URL dynamically
Embed lat & lon from getLocation() into the API URL string.
2
Add API key
Append &appid=YOUR_KEY and &units=metric to get °C.
3
GET request
Send the HTTP request to OpenWeatherMap servers.
4
Parse larger JSON
Use 4096-byte buffer (bigger payload than location).
5
Extract fields
weather[0].main → condition; main.temp → float; name → city.
6
Print output
Place, Temperature °C, and Weather type to Serial Monitor.

## Slide 7
Serial Monitor – Live Output
● ● ● Serial Monitor — 115200 baud
> Connecting...
> WiFi Connected
> {"status":"success","city":"Bengaluru",...}
> ========== LOCATION ==========
> City: Bengaluru
> Region: Karnataka
> Country: India
> Latitude: 12.98
> Longitude: 77.59
> ========== WEATHER ==========
> Place: Kanija Bhavan
> Temperature: 29.82 °C
> Weather: Clouds
WiFi
Connects to network, status printed
Location API
Raw JSON from ip-api.com
Parsed Data
City, Region, Country, Lat/Lon
Weather API
Place, Temperature, Condition

## Slide 8
APIs Used in This Project
① ip-api.com (Free · No Key Required)
URL: http://ip-api.com/json/
Response: {"status":"success","country":"India","city":"Bengaluru","lat":12.98,"lon":77.59,...}
Fields used: lat, lon, city, regionName, country
② OpenWeatherMap (Free tier · API Key needed)
URL: https://api.openweathermap.org/data/2.5/weather?lat=12.98&lon=77.59&units=metric&appid=KEY
Response: {"name":"Kanija Bhavan","main":{"temp":29.82},"weather":[{"main":"Clouds"}],...}
Fields used: name, main.temp, weather[0].main
Get your free key at: home.openweathermap.org/api_keys
Free tier: 60 calls/min, 1M calls/month

## Slide 9
Key Learnings & Takeaways
📡
WiFi on ESP32
ESP32 has built-in WiFi — just use WiFi.h. No extra hardware needed to connect to the internet.
📍
IP-based Geolocation
ip-api.com gives lat/lon from the device's public IP — free and requires no registration.
🌐
RESTful HTTP Calls
HTTPClient makes GET requests easy. JSON responses are parsed with the lightweight ArduinoJson library.
🔑
API Key Management
OpenWeatherMap requires a key stored as a String. Keep it private — don't share sketches with your key inside.
📟
Serial Monitor Debugging
Serial.print() at 115200 baud is essential for debugging. Always test with Serial before adding a display.
🔄
setup() vs loop()
Weather fetch runs once in setup(). Move getWeather() to loop() with a delay to refresh periodically.

## Slide 10
Thank You!
WiFi
OpenWeatherMap
ArduinoJson
ESP32
Arduino IDE
ESP32 Auto Weather Station · Built with Arduino IDE · Bengaluru, India